## Slide 1
Using Data Analytics on Dimensionless Numbers to Predict the Ultimate Recovery Factors For Different Drive Mechanisms in Gulf Of Mexico Oil Fields
Thesis Defense
Gowtham Talluru
Fall-2017

## Slide 2: Outline
Problem understanding
Earlier data analytical models for predicting RF
Data understanding
Data Preparation/ Feature Engineering
Modeling
  Multiple Linear Regression
  k Nearest Neighbors
  Regression Trees
  Random Forest
  Artificial Neural Network
  Ensemble model
Sensitivity Analysis
Recommendations for future work
Conclusions

## Slide 3: Data, Feature Engineering and Model
Lecture slides Dr. Wu
Notes: The three main components
Feature engineering – dependent variable may not have direct relationship with independent variables

## Slide 4: Earlier data analytical models to predict RF
Model | Equation
Guthrie and Greenberger (1955) (73 Sand stone reservoirs) | 
Arps et al (1972) (312 Sand stone reservoirs) | 
Isehunwa & Nwankwo (1994) (12 reservoirs) | 
Gulstad (1995) | 
Sharma et al (2010) (1300 reservoirs) | Multiple linear regression, PCA, Cluster Analytsis. TORIS dataset
Darhim et al (2016) (150 reservoirs) | Assigned points for technology used 4D-Seismic, 3D-Seismic, VSP, Tertiary recovery technique, Secondary recovery technique, Artificial lift etc. ANN used.
Model | Equation
Guthrie and Greenberger (1955) (73 Sand stone reservoirs) | 
Arps et al (1972) (312 Sand stone reservoirs) | 
Isehunwa & Nwankwo (1994) (12 reservoirs) | 
Gulstad (1995) | 
Sharma et al (2010) (1300 reservoirs) | Multiple linear regression, PCA, Cluster Analytsis. TORIS dataset
Darhim et al (2016) (150 reservoirs) | Assigned points for technology used 4D-Seismic, 3D-Seismic, VSP, Tertiary recovery technique, Secondary recovery technique, Artificial lift etc. ANN used.
Notes: Based on number of reservoirs
First 4 similar are LR models before 1995 while new data analytical models were not widespread
Sharma et al ( divided the RF into categories and classification techniques)

## Slide 5: Work Flow
Raw Data
  13288 Oil and Gas Reservoirs
  82 Attributes
Data Filtering
  Remove specific kind of reservoirs with very few data instances
Data processing
  Reorganize factor variables to reduce the levels
  Select categorical variables which are statistically significant
  Remove reservoirs with data errors (ORF, OIP, BHCOMP, k=0 etc)
  Select reservoirs which finished 80% of recoverable reserves.
  Check reported RF is consistent with calculated RF
  Create copies of data and use transformations appropriate for each modelling technique
  Split the data into training and test sets
Modelling
Multi linear regression, Robust regression, LASSO
kNN
Decision trees, Random forest
Artificial Neural Networks, Ensemble
  Select oil reservoirs
Notes: Data filtering
Reservoirs without wells- having ORF, zero OIP, zero k, porosity
Reservoirs having few instances( Structure, Timezone)
Reservoirs more than 80% Ultimate
Data Processing
Converting predictors into appropriate data type
Why reorganizing factor variables
Statistical significance of categorical variables

## Slide 6: Dimensionless parameters
Dimensionless number | Expression
Capillary Number (Npc) | 
Gravity Number (Ng) | 
Aspect Ratio (Rl) | 
End point mobility ratio | 
Density Number (Nρ) | 
Development factor | 
Heterogeneity factor | 
Dimensionless number | Expression
Capillary Number (Npc) | 
Gravity Number (Ng) | 
Aspect Ratio (Rl) | 
End point mobility ratio | 
Density Number (Nρ) | 
Development factor | 
Heterogeneity factor | 
Notes: A few- Mico level
A few- Macro level
Need to come up – heterogeneity, field development etc
If two reservoirs having similar dimensionless numbers should have similar recovery factors irrespective of their size and fluid properties
Baker and Swerdloff 1955--- interfacital tension

## Slide 7: Development Number
Number of wells Dev number
k Dev number
Area Dev number
Notes: Defined to characterize field development
Dimensionless
Same reservoir if Number of well inc
Two reservoris have same number of wells and perm, reservoir having higher area…..

## Slide 8: Heterogeneity Number
NTG | (Oil Area/ Total Area) | Hetro number
1 | 1 | 1
Low | 1 | High
1 | Low | High
Low | Low | Very High
Notes: We already have methods to characterize heterogeneity
In the data set we didn’t have mu

## Slide 9: Data processing
raw_data
13288 x 82
oilResClean
3038 x 82
GoM 2524 x 33
Data Filtering
Only Complete cases
Only oil Reservoirs (GOR<30)
OIP, ORF, BHCOMP,K ≠ 0
Np > 0.8 * Rec_OIP etc
Adding Dimless numbers and transformation
Add , , , , , , Mob_ratio etc
Box cox, log transformation
Centering and scaling
GoM_train 2022 x 33
GoM_test 2022 x 33
80%
20%

## Slide 10: Inspection of each predictor
Min | 1st Quart | Median | Mean | 3rd Quart | Max
0.24 | 0.58 | 0.70 | 0.85 | 0.85 | 27.05
Summary of End point Mobility Ratio
After Removing extreme values (27.05)
And log transformation
A single extreme value in the data is enough to ruin the data transformation
Notes: Each predictor had extreme values which can be considered as very different from reservoirs considered for study
Reservoirs with these kind of predictors were removed

## Slide 11: Data transformation
or
log(x)
Use log transformation if λ ≈0
Normal Transformation
Centering and Scaling
Notes: Why data needs to be transformed
Porosity—0.1
Capillary number -10^5
If used in techniques like kNN
MLR doesn’t require normalization but the beta parameters estimated cannot be compared.

## Slide 12: Dummy Variables
Reservoir | FSTRU
Res-1 | A
Res-2 | B
Res-3 | C
Res-4 | D
Res-5 | E
Res-6 | K
Reservoir | FSTRU.A | FSTRU.B | FSTRU.C | FSTRU.D | FSTRU.E | FSTRU.K
Res-1 | 1 | 0 | 0 | 0 | 0 | 0
Res-2 | 0 | 1 | 0 | 0 | 0 | 0
Res-3 | 0 | 0 | 1 | 0 | 0 | 0
Res-4 | 0 | 0 | 0 | 1 | 0 | 0
Res-5 | 0 | 0 | 0 | 0 | 1 | 0
Res-6 | 0 | 0 | 0 | 0 | 0 | 1
Notes: Why dummy vars?
To incorporate factor variables into Regression models

## Slide 13: Bias and Variance, Training and Test data sets
“Applied predictive modelling, Max Kuhn & K Johnson
Optimum model
Complexity
80% Train data, 20% Test data
Notes: Bias is how much the model deviates from original data
Variance is how flexible model is , Weightage to outliers
If we keep increasing the flexibility
So test data set is separated to evaluate models with different bias and variance
While separating test data, the distribution of target variable should be same in both

## Slide 14: Linear regression and its cousins
Model | Contribution of each observation to loss function
Ordinary least squares regression | 
Least absolute value regression. | 
Huber loss function | 
Ridge regression | 
Least absolute shrinkage operator (LASSO) | 
Elastic net regression | 
Model | Contribution of each observation to loss function
Ordinary least squares regression | 
Least absolute value regression. | 
Huber loss function | 
Ridge regression | 
Least absolute shrinkage operator (LASSO) | 
Elastic net regression | 
Pros
Easy to interpret
Easy to compare the weightage of predictors
Cons
Non linear interactions
Highly correlated predictors
No bounds on target
Notes: Various variants of linear regression.
The main difference is definition of error function and balance between bias and variance
OLR has more variance or it gives relatively more importance to extreme points

## Slide 15: Closed form solution – OLS Regression
Ordinary least squares regression | 
Ordinary least squares regression | 
β
High Correlation between predictors
No. of predictors greater than No. of observations.
X β + ε
ε

## Slide 16: Removing highly correlated predictors
Notes: Specific gravity and density number
Dip number and Effective aspect ratio

## Slide 17: Modelling- Multiple linear Regression
Beta Coefficients of numeric predictors
Numeric Predictor | Beta
Intercept | 0.368
Porosity | -0.008
End point mobility ratio | 0.030
Nalpha | -0.076
Ng | -0.181
Npc | -0.068
Dev_factor | 0.145
Hetro_factor | -0.016
Beta Coefficients of dummy categorical predictors
Categorical Predictor | Beta
FSTRU.A | -0.019
FSTRU.B | -0.039
Play_type.A1 | 0.028
Play_type.F1 | -0.033
DRIVE.COM | -0.015
DRIVE.DEP | -0.044
RES_TYPE.N | 0.021
FSTRU.A - Anticline
FSTRU.B - Fault
DRIVE.COM – Combination drive
DRIVE.DEP – Depletion drive
DRIVE.WTR – Water drive (Base case)
Out of 31 predictors
Root mean square error (RMSE) | 9%
Mean absolute error (MAE) | 7%
Notes: Beta coefficients of highly significant predictors

## Slide 18: LASSO
Log(λ)
Mean Absolute Error
Least absolute shrinkage operator (LASSO) | 
Least absolute shrinkage operator (LASSO) | 
β
No. of non negative beta coefficients
Notes: Do we need 31 predictors?
If we have highly collinear predictors
LASSO acts somewhat similar to PCA to reduce the dimensionality
If lambda increases beta coefficients of irrelevant predictors reduces to zero.

## Slide 19: LASSO
Log(λ)
Co efficient
No. of non negative predictors

## Slide 20: LASSO
Coefficient | Value
(Intercept) | 0.346
Dev_factor | 0.071
PLAY_TYPE.A1 | 0.013
FSTRU.C | 0.003
BHCOMP | -0.002
Hetro_factor | -0.005
DRIVE.COM | -0.008
Nalpha | -0.036
Npc | -0.041
DRIVE.DEP | -0.051
Ng | -0.086
No.of Predictors | 11
λ | 0.0098
MAE | 9.5%
RMSE | 11.0%

## Slide 21: Multiple Linear regression- Predicted vs original ORF
Negative ORF
Fitted Values
Residuals
Predicted
Original ORF
Notes: Tow issues
Negative ORF
Trend in the residuals indicates presence of non linear interaction

## Slide 22: Modelling Non Linear Interactions
Structure of Reservoir :
Density Number
Heterogeneity: Mobility Ratio
Drive : Capillary Number
Structure of Reservoir : Gravity Number
Drive : Gravity Number
FSTRU.E : Density Number
FSTRU.C : Mobility_Ratio_endpoint
DRIVE.DEP : Dev_Number
Dev_factor : Hetro_factor
Ng : Npc
Drive.DEP : Npc
RMSE | 10%
MAE | 7%
Notes: It is not necessary that each dimless have same effect in every reservoir
Resevoirs with high dip – gravity number
Reservoir with high heterogeneity – mobility ratio

## Slide 23: Modelling- Regression trees
Notes: One way Non linear interactions
Explicitly adding them to model
Another way is models predicting them implicitly
Regression tree splits the data by applying rules on predictors such that the leaf nodes least within sum of squares

## Slide 24: Regression trees size
Optimum tree length
Cp
X val relative error
Tree size
Notes: The algorithm will keep splitting the data until the ratio of SSE is greater than Cp
The size of regression tree with low Cp will be high.
To determine the optimum tree size we plot
As the tree size increases error decreases and then increases due to overfitting

## Slide 25: Modelling- Regression trees
Tree Size | 6
Tree Size | 20
Train
Data
Test
Data
RMSE | 13%
MAE | 10%
Notes: At low tree size, the output has only few levels
As the size of the tree increases---- tends to replicate the original trend

## Slide 26: Modelling – Random Forest
Ensemble of many decision trees
Each split in each tree is made upon randomly selected “m” parameters.
m → N Random Forest → Single decision tree
Outcome is average of all the trees
RMSE | 11
MAE | 9
m | 3
No. of Tree | 500
Notes: Random forest adds flexibility to decision tree

## Slide 27: Modelling – Artificial Neural Network
Hidden
Layer
Predictor
Variables
Bias
Target
variable
Hidden
Layer
Notes: ANN tries to emulate
Inmplicitly predict nonlinear interactions
Each arch has a weitage

## Slide 28: Modelling – Artificial Neural Network
RMSE | 9%
MAE | 6%

## Slide 29: Ensemble modelling
Notes: MLR poor low ORF
RF better than ANN at high ORF

## Slide 30: Ensemble modelling
RMSE | 6.3%
MAE | 4.6%

## Slide 31: Sensitivity Analysis- No of wells

## Slide 32: Sensitivity Analysis- Porosity

## Slide 33: Discussion
Model | RMSE | MAE | Remarks
Multiple linear Regression | 9.0% | 7.0% | No restriction on predicting negative ORF
Robust linear Regression | 9.3% | 7.2% | Poor performance at extremes
LASSO | 11.0% | 9.5% | Can select top predictors and ignore irrelevant predictors
Regression Tree | 13% | 10% | Model non linear interactions upto limited extent
Random Forest | 11.1% | 9.0% | No absurd predictions Black box model
Artificial Neural Network | 8.5% | 6.0% | Automatically simulates non linear interactions. Black box model
Ensemble Model | 6.3% | 4.6% | Combines strengths of above models

## Slide 34: Recommendation for further work
Predictor | Co efficient
 | a
 | b
 | c
Predictor | Co efficient
 | a
 | b
 | c
Minimize objective function
Minimize objective function
Parameter estimation using MLE
)

## Slide 35: Conclusions
Dimensionless numbers can be used to scale data analytical models to predict Ultimate recovery factor and Reservoir performance. They makes the model applicable to new data and also to reservoirs out of study area.
There is always compromise between complexity of the model and interpretability. Multiple linear regression model could be easily interpreted, but cannot model non linear interactions implicitly. Regression trees can model non linear interactions only up to limited extent. ANN model acts like a black box but can model non linear interactions implicitly
Models using parameter estimation with MLE can connect physics and mathematics in a better way.

## Slide 36: Thank You

## Slide 37: Back up

## Slide 38: Regression trees – Variable Importance
  Pros
Easy to interpret and understand
No pre processing of the data
Robust to outliers
Importance of predictors
Cons
High bias
Stability

## Slide 39: Modelling- k Nearest Neighbours
Identifies nearest neighbors based on distance metric
Target variable – summary statistic of nearest neighbors
Scaling and centering predictors
Method | Distance Expression
Euclidean distance | 
Murkowski distance | 
Manhattan distance | 
Method | Distance Expression
Euclidean distance | 
Murkowski distance | 
Manhattan distance | 
Euclidean distance is used in the model

## Slide 40: Modelling- k Nearest Neighbours
Chart: RMSE, MAE vs No. of Neighbours
| 1 | 5 | 10 | 25 | 50 | 100 | 200
RMSE | 0.168 | 0.134 | 0.128 | 0.127 | 0.129 | 0.132 | 0.135
MAE | 0.129 | 0.108 | 0.105 | 0.106 | 0.108 | 0.111 | 0.113
Optimum number of neighbors - 10
No negative ORF predicted
Missed trend due to the presence of complex relationships between predictors.
RMSE | 12.8%
MAE | 10.5%

## Slide 42: Data sets for different models
Outliers
Data set | Dimensions | Modelling Techniques
GoM_Original | 2524 x 18 | Decision Tree, Random Forest
GoM_processed | 2514 x 33 | Linear Regression Variants, ANN
GoM_proc_nooutliers | 2423 x 33 | Linear Regression Variants, ANN

## Slide 46
[1] "FSTRU.A" "FSTRU.B" "FSTRU.C" "FSTRU.D"
[5] "FSTRU.E" "FSTRU.K" "PLAY_TYPE.A1" "PLAY_TYPE.F1"
[9] "PLAY_TYPE.F2" "PLAY_TYPE.P1" "CHRONOZONE2.MIOCENE" "CHRONOZONE2.PLEISTOCENE"
[13] "CHRONOZONE2.PLIO_UPR" "DRIVE.COM" "DRIVE.DEP" "DRIVE.PAR"
[17] "DRIVE.WTR" "RES_TYPE.N" "RES_TYPE.S" "RES_TYPE.U"
[21] "POROSITY" "SW" "BHCOMP" "Mobility_Ratio_endpoint"
[25] "Nalpha" "Np" "Ng" "Npc"
[29] "Dev_factor" "Hetro_factor" "ORF"

## Slide 47
FSTRU | Dip Angle
A / Anticline | 10
B / Fault | 11
C / Sallow Salt diapir | 12
D / Intermediate Salt diapir | 13
E / Deep Salt dome | 14
F / Salt Ridge | 15
G/ Shale diapir | 16
H/ Unconformity | 17
I/ Stratigraphic | 18
J/ Reef | 19